## Slide 1
A Novel Cache-Utilization Based Dynamic Voltage Frequency Scaling (DVFS) Mechanism for Reliability Enhancements
*Yen-Hao Chen, *Yi-Lun Tang, **Yi-Yu Liu, ***Allen C.-H. Wu, *TingTing Hwang
*National Tsing Hua University, Taiwan **Yuan Ze University, Taiwan ***Jiangnan University, China
Notes: Thank you Mr. CHAIR. The title of my presentation is “a novel cache-utilization based dynamic voltage frequency scaling (DVFS) mechanism for reliability enhancements”.

## Slide 2: Outline
Background & motivation
  Dynamic voltage frequency scaling (DVFS)
  7T/14T SRAM cache [1]
Cache-utilization based voltage frequency scaling mechanism
  Online control scheme
  Tag copy operation
Experimental results
Conclusions
Notes: This is the outline. First, we discuss the background and the motivation. And then, we introduce the cache utilization-based voltage frequency scaling mechanism. Finally, the experimental results and conclusions.
Let’s start with the background and the motivation.

## Slide 3: Dynamic Voltage Frequency Scaling
Many modern processor designs have supported DVFS to reduce the power consumptions
SRAM cache may become very unreliable under the near-threshold supply voltage
Most DVFS frameworks suffer from the limitation of the lowest supply voltage constraint due to the reliability of the SRAM cache
Chart: Supply voltage vs power consumption
| 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
Power consumption | 0.0256 | 0.0625 | 0.1296 | 0.2401 | 0.4096 | 0.6561 | 1

## Slide 4: 7T/14T Reconfigurable SRAM [1]
Tradeoff between capacity and reliability under the near-threshold supply voltage
  Use two additional transistors and a /CTRL
  Connect two SRAM cells into a single robust one
/CTRL
Wordline 0
Wordline 1
Bitline
/Bitline
Notes: A 7T/14T reconfigurable SRAM cache has been proposed. It tradeoffs the capacity for reliability enhancements under the ultra-low supply voltage condition.
It connects two conventional 6T SRAM cell together into a single robust SRAM cell by two additional transistors and a control line.

## Slide 5: 7T/14T Reconfigurable SRAM [1] (cont.)
/CTRL
Operate in three modes
  Regular cache
    Normal mode
  Line-merged cache
    High-speed mode
    Dependable low-power mode
 | Regular cache | Line-merged cache | 
Mode | Normal | High-speed | Dependable low-power
Cache capacity | Regular (4-way) | Half (2-way) | Half (2-way)
Access latency | Regular (4 cycles) | Faster (3 cycles) | Regular (4 cycles)
Reliable voltage | Regular (0.75v) | Regular (0.75v) | Better (0.55v)
Wordline 0
Wordline 1
Bitline
/Bitline
Notes: By controlling the control line and wordlines, 7T/14T SRAM cache can operate in three operation modes. First, the normal mode or we call it regular cache. It turns off the two additional transistors, and two conventional 6T SRAM cells can operate independently.
And, line-merged cache, 7T/14T SRAM connects two SRAM cells together and halves its capacity to obtain faster speed or better reliability, namely high-speed mode or dependable low-power mode.

## Slide 6: Motivation
But reducing cache capacity may…
  Increase cache miss rate
  Result in performance and energy penalties
It motivates us to…
  Investigate the inter-relationship between…
    The computational patterns in execution
    The cache utilization
  Devise an effective online control scheme
    Switch operation modes of 7T/14T SRAM cache
    Enhance reliability
    Minimize performance and energy penalties
Chart: Cache miss rate
| Full-sized capacity | Half-sized capacity
Cache miss count | 30 | 90
Notes: So, we can reduce the cache capacity to obtain better SRAM reliability. But reducing cache capacity may increase cache miss rate and result in performance energy penalties.
By the above observations, it motivates us to investigate the inter-relationship between the computational patterns in execution and the cache utilization. Also, we want to devise an effective online control scheme that can switch the 7T/14T SRAM cache operation modes for reliability enhancements with minimized performance and energy penalties.

## Slide 7: Outline
Background & motivation
  Dynamic voltage frequency scaling (DVFS)
  7T/14T SRAM cache [1]
Cache-utilization based voltage frequency scaling mechanism
  Online control scheme
  Tag copy operation
Experimental results
Conclusions
Notes: Now let’s discuss the cache utilization-based voltage frequency scaling mechanism.

## Slide 8: Online Control Scheme
The next operation mode is decided by the computational pattern of the last time period
High-speed
Normal
time
Computational pattern
Operation mode
Time period
Executing
Executing
Executing
Executing
Normal
Patterns
Patterns
Dependable low-power
Patterns
Control Scheme

## Slide 9: The Proposed Control Scheme
Two metrics are used to decide the operation mode
  Miss per kilo instructions (MPKI)
  Overhead cycles
True
True
False
False
MPKI > Threshold
Overhead cycles < 0
Dependable low-power mode
High-speed mode
Normal mode
Three operation modes of 7T/14T SRAM cache
Control Scheme
Notes: 7T/14T SRAM cache has three operation modes, which are normal mode, high-speed mode and dependable low-power mode. We use two metrics to decide the operation mode, which are the miss per kilo instructions (MPKI) and the overhead cycles.
Let’s start with the first metric, MPKI.

## Slide 10: MPKI Metric
Chart: Performance penalty in dependable low-power mode
| Low MPKI applications | High MPKI applications
Normalize CPI | 0.62195 | 0.97418
High MPKI applications can be switched to the dependable low-power mode for energy saving
  Not sensitive to the CPU core frequency
  Low cache utilization, i.e. low data locality
Performance penalty
Dependable low-power mode
High-speed mode
Normal mode
True
True
False
False
MPKI > Threshold
Overhead cycles < 0
Notes: High MPKI applications are not sensitive to the CPU core frequency and usually shows low cache utilization, that is, not much data locality.
By our experiment, low MPKI applications show severe performance penalty in dependable low-power mode. On the other hand, the affection on the high MPKI applications is relatively small in dependable low-power mode. So, by the observations, we conclude that MPKI is a good metric to decide whether to enter the dependable low-power mode.
Next, we use ‘overhead cycles’ to decide whether to enter the high-speed mode or normal mode.

## Slide 11: Overhead Cycles Metric
Cycle differences of normal and high-speed modes
    Additional cycles caused by capacity loss
      : Additional cache misses by capacity loss
    Reduced cycles in high-speed mode
      : Reduced cache latency in high-speed mode
Dependable low-power mode
High-speed mode
Normal mode
True
True
False
False
MPKI > Threshold
Overhead cycles < 0
Notes: The overhead cycles are defined as the cycle differences between normal mode and high-speed mode, which is calculated as the cycle cost subtract cycle benefit. And, cycle cost is the additional cycles that caused by capacity lost, calculated by the delta miss count times the miss penalty. And, the cycle benefit is the reduced cycles gained from high-speed mode, calculated by the load/store instruction count times the delta cycles of the high-speed mode.
This is our overall control scheme. Those metrics are easy to obtain in the modern processors except for the delta miss count. For the next pages, we are going to discuss how to obtain the delta miss count by examples.
𝑪𝒚𝒄𝒍𝒆_𝒄𝒐𝒔𝒕: Additional cycles that caused by the capacity lost
  The increased L1 miss count times the average L2 cache latency
  𝑪𝒚𝒄𝒍𝒆_𝒄𝒐𝒔𝒕=〖𝜟𝒎𝒊𝒔𝒔\_𝒄𝒐𝒖𝒏𝒕〗_𝑳𝟏×〖𝒂𝒗𝒈\_𝒄𝒚𝒄𝒍𝒆〗_𝑳𝟐
〖𝑪𝒚𝒄𝒍𝒆〗_𝒃𝒆𝒏𝒆𝒇𝒊𝒕: Reduced cycles gained from high-speed mode
  The read/write instruction count times the reduced L1 cache latency
  〖𝑪𝒚𝒄𝒍𝒆〗_𝒃𝒆𝒏𝒆𝒇𝒊𝒕=〖𝑰𝑪〗_𝒓𝒘×𝚫〖𝒄𝒚𝒄𝒍𝒆〗_𝑳𝟏

## Slide 12
Hit in regular cache but miss in line-merged cache
  Capacity loss
time
Time period
Executing
Line-merged cache
Regular cache
The next operation mode
- )
Truly, we have to obtain the regardless of the current operation mode
Mode
Control Scheme

## Slide 13: in Regular Cache
  Record hit count in LRU, lru blocks
  When hit in the LRU, lru blocks (cache hit)
    Increase the miss counter
  When miss
    Do not increase the miss counter
MRU
mru
= 0
= 1
hit
mru
lru
lru
LRU
C
B
A
D
LRU
MRU
LRU sequence
Notes: Obtaining the delta miss count in regular cache is easy. We can just count the hits on the lru blocks.
For example, when a hit in the LRU block, we increase the miss counter and update the lru sequence. By doing so, we can obtain the delta miss count in regular cache.

## Slide 14: in Line-Merged Cache
Data array is reduced to half
  Only way 0 and way 1 have data in data array
Full-sized tag array can still be used
  To maintain full-sized tag information
A
MRU
B
mru
C
lru
D
LRU
A
B
Tag array
Data array
Way 0
Way 1
Way 2
Way 3
A
B
Blocks with data
Regular cache
Line-merged cache
C
D
Notes: When in line-merged cache, the capacity of the data array reduces to half.
In this case, only way 0 and way 1 have data. But, we can still use the full sized tag array to maintain the full-sized cache replacement policy information and obtain the delta miss count.

## Slide 15: in Line-Merged Cache
Simulate full-sized cache replacement policy
  When hit in the LRU, lru blocks (cache miss)
    Increase the miss counter
    Evict the cache block
    Copy the evicted tag to appropriate location
D
mru
MRU
LRU
lru
C
Evict block B, fetch block D
Evict block A, fetch block E
MRU
mru
lru
LRU
Tags with data in data array
= 0
= 1
hit
miss
LRU sequence
B
D
E
A
Notes: For examples, when a hit in the LRU block, it actually is a cache miss, because we don’t have the data in the data array. Besides of increasing the miss counter, we have to copy the evicted tag information into the appropriate location to maintain the replacement policy information of the full-sized cache. And then, update the LRU sequence.
Similarly, when a miss, we have to copy the evicted tag information to the appropriate location to maintain the replacement policy information of the full-sized cache. And then, update the LRU sequence. With the replacement policy information of the full-sized cache, we can obtain the delta miss count.

## Slide 16: Support for Tag Copy Operation
Memory address
Index
Offset
Tag
Tag buffer
Decoder
Tag array Way 0
Write/Sense
Decoder
Tag array Way 1
Write/Sense
Decoder
Tag array Way 2
Write/Sense
Decoder
Tag array Way 3
Write/Sense
hit?
hit?
hit?
hit?
Copy tag B from way 1 to way 3
D
C
A
Tags with data array
D
C
A
hit
B
D
B
Notes: To performance the tag copy operation, we modify the cache architecture.
This is a conventional cache tag array.
When comes a memory request, the index will be sent to the decoders and the tag will be compared with the tags in the tag array to determine whether it is a hit or not. And, update the tag into the tag array if necessary.
Now, if we want to copy tag B from way 1 to way 3, a tag buffer is required to temporally store the tag B, and then, written to the way 3. And finally, we can update the way 1 by the address of original memory request.
This is the overall schematic.

## Slide 17: Overhead Analysis of Tag Copy Operation
Small hardware area overhead
  A tag buffer
  Two multiplexers
No timing delay overhead
  Not on the critical path
    One tag access cycle delay
    Paralleled with data fetching from next level memory
Notes: The hardware overhead of our modification is relatively small, only a tag buffer and two multiplexers. And, there is no timing overhead, because it only takes one tag access cycle delay and can be performed in parallel with the data fetching from the next level memory hierarchy.

## Slide 18: Outline
Background & motivation
  Dynamic voltage frequency scaling (DVFS)
  7T/14T SRAM cache [1]
Cache-utilization based voltage frequency scaling mechanism
  Online control scheme
  Tag copy operation
Experimental results
Conclusions
Notes: Next, the experimental results.

## Slide 19: Configurations
Reference
  No DVFS with conventional 6T SRAM cache
Online DVFS (0.75V) [16]
  A DVFS mechanism using safe supply voltage
Online DVFS (0.55V)
  The online DVFS using near-threshold voltage
CUB VFS (0.55V)
  The proposed cache-utilization based voltage-frequency scaling mechanism with the 7T/14T SRAM cache using near-threshold voltage
Notes: We performed four configurations, including the reference configuration using the conventional 6T SRAM cache, conventional online DVFS using safe supply voltage and conventional online DVFS using the near-threshold voltage, and finally our proposed cache utilization-based voltage-frequency scaling mechanism with 7T/14T SRAM cache using the near-threshold voltage.

## Slide 20: The Reliability Comparisons
CUB VFS can guarantee reliable operations
  When using the near-threshold supply voltage
Chart: Bit errors per day
| mix1 | mix2 | mix3 | mix4 | mix5 | mix6 | mix7 | mix8 | mix9 | mix10 | mix11 | mix12 | mix13 | mix14 | mix15 | mix16 | mix17 | mix18 | mix19 | mix20 | mix21 | mix22 | Avg.
Online DVFS (0.75V) | 7.9395 | 3.4432 | 5.5707 | 4.0198 | 9.877 | 6.8609 | 8.4506 | 4.0735 | 1.149 | 7.6588 | 5.4277 | 9.2747 | 5.9727 | 5.1797 | 12.3925 | 6.4329 | 7.2237 | 4.7578 | 3.6068 | 4.3147 | 11.6973 | 7.7926 | 6.2224
Online DVFS (0.55V) | 26579.3378 | 14714.3774 | 16832.5647 | 17202.32 | 42611.798 | 26663.3053 | 39130.8208 | 12510.5562 | 2231.8464 | 24887.902 | 21022.7538 | 33536.4929 | 23351.2325 | 18673.8587 | 42887.0681 | 22171.2827 | 26997.6498 | 14978.8219 | 17586.88 | 9501.8769 | 48600 | 25176.0548 | 22949.9479
CUB VFS (0.55V) | 4.4432 | 1.2107 | 1.7308 | 0 | 1.6076 | 0.26285 | 0.43221 | 0.2956 | 0 | 1.6873 | 4.4031 | 2.8893 | 1.954 | 5.1859 | 3.9258 | 3.7753 | 2.6264 | 0.21671 | 1.8949 | 0.30037 | 3.8621 | 3.7531 | 2.0199
Reliable [21]
Un-reliable
Notes: This is the reliability comparisons. The conventional online DVFS can guarantee reliable operation under the safe supply voltage, but when using the near-threshold voltage, it becomes unreliable. On the other hand, our proposed mechanism can guarantee a reliable operation under the near-threshold voltage.

## Slide 21: The Performance and Energy Overheads
2.6%
Chart: Weighted speedup
| Reference | Online DVFS (0.75V) | Online DVFS (0.55V) | CUB VFS (0.55V)
Weighted speedup | 3.4762 | 3.3941 | 3.3941 | 3.5671
Energy (normalized to reference) | 1 | 0.88233 | 0.83969 | 0.83711
CUB VFS incurs no performance/energy overheads
  Even slightly better
4.5%
5.1%
Notes: Next we want to understand the performance and energy overheads of our proposed mechanism. By the results, it shows that our proposed mechanism incurs no performance or energy overhead, or even slightly better.
Our proposed mechanism outperforms the reference configuration by 2.6% and outperforms the online DVFS configuration by 5.1%. Also, our proposed mechanism achieve 4.5% more energy saving compared to the online DVFS configuration.

## Slide 22: Outline
Background & motivation
  Dynamic voltage frequency scaling (DVFS)
  7T/14T SRAM cache [1]
Cache-utilization based voltage frequency scaling mechanism
  Online control scheme
  Tag copy operation
Experimental results
Conclusions
Notes: Finally the conclusions.

## Slide 23: Conclusions
A cache utilization-based dynamic voltage frequency scaling mechanism for reliability enhancements is proposed
  Adopt reconfigurable 7T/14T SRAM cache
  Greatly reduce the bit-error probability
  Effectively control operations in a reliable state
  Pay no performance or energy penalties
Notes: A cache-utilization based dynamic voltage frequency scaling mechanism for reliability enhancements is proposed. It adopts reconfigurable 7T/14T SRAM cache and can greatly reduce the bit error probability. And, it effectively operates in a reliable condition without paying any performance or energy penalties.

## Slide 24
Thank you for listening
Notes: This is my presentation. Thank you for listening.

## Slide 25
Backup Slides

## Slide 26: Examples of Modified Placement Policy

## Slide 27: Experimental Environment
GEMS simulator
Quad-core system, Linux kernel 2.6.15
20 randomly mixed workloads from SPEC CPU 2006
 | Normal mode | Dependable low-power mode | High-speed mode
Supply voltage | 0.8V | 0.55V | 0.8V
CPU frequency | 800 Mhz | 400 Mhz | 800 Mhz
L1 cache size | 32KB | 16KB | 16KB
L1 cache assoc. | 8 way | 4 way | 4 way
L1 cache latency | 4 cycles | 4 cycles | 3 cycles
L2 cache | 256KB, 8 way, 20 cycles |  | 
DRAM cycles | 300 | 150 | 300