## Slide 1: Dynamic Random Access Memory (DRAM) Basic
Yen-Hao Chen
yhchen@cs.nthu.edu.tw

## Slide 2: DRAM Cell Arrays (Mats)
Column decoder
Column decoder
Column decoder
Row decoder
Sense amplifier
Row decoder
Sense amplifier
Row decoder
Sense amplifier
Accessing DRAM cell array data, include address and command decoding, bit line sensing, data I/O transport
Row decoder
Sense amplifier
Column decoder
Address
Command
Command, address transport
1. In bank data movement
I/O bus
2. System data transport
I/O gating
Read data latch
Write drivers

## Slide 3: The Operation of DRAM
Command
Data IO bus
Activate
Read
Precharge
Activate
Turn on the transistor The charge in the capacitor drives the bit line voltage
The sense amplifier differentiate the voltage to VCC or VSS
Bit lines are fully charged or discharged over time to store the latched data back into the cells in the open row
Turn off the transistor
Precharge the bit lines to (VCC+VSS)/2
Bit line voltage
Word line
Bit line
Capacitor
Transistor

## Slide 4: Timing Parameters
tRAS
tRP
tRC
tRCD
tCAS
tBurst
tAC
Command
Data IO bus
Activate
Read
Precharge
Activate
tRAS: row access strobe
tRP: row precharge
tRC: row cycle (tRAS + tRP)
tRCD: row to column command delay
tCAS: column access strobe latency
(tCL), (tAA)
tBurst: data burst duration (tB)
tAC: access time (tRCD + tAA)