## Slide 1: Communication Driven Remapping of Processing Element (PE) in Fault-tolerant NoC-based MPSoCs
Chia-Ling Chen, Yen-Hao Chen and TingTing Hwang Department of Computer Science National Tsing Hua University, Taiwan

## Slide 2: Outline
Multi-Processor System-on-Chip (MPSoC)
  Task remapping for fault-tolerant
Communication driven remapping method
  Model communication cost on edges
  Allow tasks be moved to non-neighboring PEs
Initial mapping improvement
Experimental results
Conclusions
Notes: This is the outline.
First, we are going to talk about the multi-processor system-on-chip (MPSoC) and its task remapping for fault-tolerant technique.
And then, we will present our proposed communication driven remapping method including its four interesting features.
Finally, we will do the experimental result and conclusions as the ending of this presentation.
Let’s start with the multi-processor system-on-chip.

## Slide 3: Multi-Processor System-on-Chip
Processing elements (PEs) integrated on a chip
  Each PE can execute a task independently
  Redundant PEs are included for fault tolerance
R1
R3
R2
R4
R6
R5
MPSoC
PE
R3
R6
Redundant PE
Notes: A multi-processor system-on-chip is a chip with several processing elements, or so called PEs, integrated on it.
Other than the normal PEs, we may integrate some other redundant PEs for fault tolerance.
Each normal PE and redundant PE can operate and execute a task concurrently.

## Slide 4: Task Graph
Application is partitioned into several tasks
  Task (node) – basic executable unit
    Must be mapped to a good PE for execution
  Edge – communication overhead
    The amount of data (data size) transferred between tasks
    A shorter edge (transferred distance) is preferred
      For lower communication overhead
R1
R3
R2
R4
R6
R5
10
5
20
10
MPSoC
R3
R6
App.
A
B
C
D
Task
Communication between tasks
Notes: To utilize the parallelism of MPSoC, applications are usually partitioned into tasks graph.
A task or node in the graph is a basic executable unit of the application and must be mapped to a good PE for execution.
The edge of the graph representing the communication overhead of the tasks. We would like to shorter the edge distance to reduce the overhead.

## Slide 5: Task Mapping
Process of deciding PE of each task for execution
Mapping with shorter transferred distance
  Less communication overhead
    Improve system performance
    Decrease energy consumption
R1
R3
R2
R4
R6
R5
10
R3
R6
A
B
R1
R3
R2
R4
R6
R5
10
R3
R6
A
B
Transferred distance = 1
Transferred distance = 2
Notes: The task mapping is the processes of determining the PE of each task for execution.
A good mapping with lower communication overhead can improve system performance and decrease energy consumption.
Take those two mappings as example, the right hand size mapping seems to have longer communication distance. Thus, we will say that the left hand size mapping seems to be a better mapping.
This is a commonly used metric to calculate the communication cost which is the summation of the transferred data size times the transferred distance.
By the metric, communication cost of the left hand side mapping is 50.
And, the communication cost of the right hand side mapping is 75.
So, once again, since the left hand side mapping has less communication overhead, we will say that the left hand side mapping is a better mapping.

## Slide 6: Communication Cost Metric
  Size – transferred data size
  Distance – transferred distance
R1
R3
R2
R4
R6
R5
10
5
20
10
R3
R6
A
B
C
D
R1
R3
R2
R4
R6
R5
10
5
20
10
R3
R6
A
D
C
B
Transferred distance = 1
Transferred distance = 2

## Slide 7: Task Remapping for Fault-tolerant
Source
Remap all tasks again when faulty PE detected
  Topology graph construction
    Repairing path
      Each path from source to target is a remapping
    Minimum-cost flow algorithm (MCF)
      To obtain repairing paths
R1
R2
R3
R4
R5
R6
Target
R1
R3
R2
R4
R6
R5
R1
R2
R4
R5
R6
R3
R1
Faulty PE
Notes: OK, when a faulty PE is detected in field, we have to remap all tasks to good PEs again to make the multiple processor system provide the expected function.
The method of finding a reconfiguration mapping usually uses the minimum-cost flow algorithm (MCF).
By adding a source node to the faulty PE and a target node to the redundant PEs, a topology graph is constructed.
Each path from the source node to the target node is a valid remapping solution, we called it “repairing paths.”

## Slide 8: Repairing Paths
A repairing path represents a remapping solution
  E.g. R1->R2->R3
  E.g. R1->R4->R5->R6
R1
R3
R2
R4
R6
R5
R1
R2
R3
R4
R5
R6
Source
Target
Faulty PE
R1
R3
R2
R4
R6
R5
Faulty PE
A
B
C
D
A
B
C
D
Notes: For example, a repairing path from source, R1, R2, R3, to target node represents a remapping which indicates that the task originally in R1 moves to R2 and the task originally in R2 moves to R3.
For another example, a repairing path from source, R1, R4, R5, R6 to target node represents a remapping which indicates that the task originally in R1 moves to R4 and the task originally in R4 moves to R5 and the task originally in R5 moves to R6.

## Slide 9: Problem Description
Each repairing path indicates a valid remapping
  All can successfully remap all tasks to good PEs
But, the remappings have different
Thus, we would like to find the repairing path with minimized communication cost
R1
R3
R2
R4
R6
R5
A
B
C
D
10
5
10
20
R1
R3
R2
R4
R6
R5
A
B
C
D
10
5
10
20
R1
R2
R3
R4
R5
R6
Source
Target
R1
R2
R3
R4
R5
R6
Source
Target
Notes: Thus, all repairing paths on the topology graph can successfully remap all tasks to good PEs.
But, the remappings have different communication costs.
Thus, we would like to find a repairing path with minimized communication cost on the topology graph.

## Slide 10: Previous Work [1]
The communication cost is modeled on nodes
  Not precise enough to represent
Tasks can be only moved to neighboring PEs
  Guarantee
  Reduce repair rate
R1
R3
R2
R4
R6
R5
10
5
10
20
R2
R4
R5
Source
Target
20
15
20
35
10
5
10
20
R1
R3
R6
(not optimal)
A
B
C
D
Notes: In previous work, they minimize the communication overhead by modeling the communication on nodes.
Take this figure as an example, the task A communicates with task B and C with data size 10. Then, the cost of R1 is 20. For the task B, it communicates with task A and C with data size 10 and 5. Thus, the communication cost the R2 is 15. And, for task C, it communicates with task A, B and D with data size 10, 5 and 20. So, the communication cost of R4 is 35. And lastly the task D, it communicates only with task C with data size 20. So, the communication cost of the R5 is 20.
Also, they guarantee the delta transferred distance is one by restricting the faulty PE can be only replaced by the neighboring PEs.
But, the previous method comes with some weakness.
First, it does not precisely represent the communication cost, since the cost is modeled on the nodes. For this example, the previous method cannot find the optimal solution.
Second, the tasks are restricted to move to neighboring PEs. This will limit the solution space and reduce the repair rate.

## Slide 11: Outline
Multi-Processor System-on-Chip (MPSoC)
  Task remapping for fault-tolerant
Communication driven remapping method
  Model communication cost on edges
  Allow tasks be moved to non-neighboring PEs
Initial mapping improvement
Experimental results
Conclusions
Notes: By the above observation, we want to propose a communication driven remapping method.

## Slide 12: Features of Our Method
Model communication cost on edges
  Precisely model the communication overhead
Allow task be moved to non-neighboring PEs
  Greatly increase the repairing flexibility
  Achieve 100% repair rate across all test cases
Notes: Our method comes with four main features.
First, it models the communication cost on edges to precisely present the communication overhead. Second, it allows the tasks move to non-neighboring PEs. We will show that this feature greatly increases the repairing flexibility and achieve 100% repair rate across all test cases. Third, the method prevents down-and-up or back-and-forth paths to avoid some unwanted corner cases. Finally, we will show that our method can further be used to reduce the communication overhead of initial mappings.

## Slide 13: Flow Diagram of Task Remapping
Repairing is applied when detecting faulty PE
Mapping
R1
R3
R2
R4
R6
R3
R6
R5
Faulty PE detected
Initial mapping
Apply MCF to obtain repairing path
Construct the topology graph
Remap the tasks
Repairing algorithm
New mapping
Execution
Mapping
Execution
10
5
20
10
D
B
A
C
10
5
20
10
A
B
C
D
Notes: Before the features, we are going to discuss the flow of the task remapping.
At the beginning, an initial mapping is used to execute the program.
When the system detects a faulty PE, the current mapping will be send to the repairing algorithm. And, the algorithm will construct the topology graph, apply the MCF to obtain repairing path, and, finally, use the remapping to remap the tasks.
And the system can keep on its execution.

## Slide 14: Communication Cost Model on Edges
R1
R3
R2
R4
R6
R5
Increment in when task remapped to PE
10
5
10
20
R1
R2
R3
R4
R4
R3
Source
Target
0
15
-15
20
0
5
5
20
0
15
is
10
5
10
20
(optimal)
A
B
C
D
Notes: The first feature of our method is that the communication cost is modeled on edges.
This will more precisely model the communication overhead.
Take the Task B as an example, if it moves to R3, the communication cost will increase 15. Take task A as another example, if it moves to R2, the communication cost will not increase. Thus, the corresponding communication overhead is 0. Similarly, we can obtain all the cost of the topology graph.

## Slide 15: Tasks moved to Non-neighboring PEs
Explore larger solution space
Achieve higher repair rate
  100% repair rate for all experimental cases
R1
R2
R3
R4
R5
R6
Source
Target
Chart: Number of faulty PEs
| 0 | 1 | 2 | 3 | 4
Previous work [1] | 1 | 1 | 1 | 0.998 | 0.986
Ours | 1 | 1 | 1 | 1 | 1
Notes: The second feature of our method is that replacement by non-neighboring PEs is allowed.
This can explore larger solution space.
By our experiment, our method achieves 100% repair rate for all test cases, meanwhile the previous method shows the degradation on high number of faulty PEs.

## Slide 16: Problem on Down-and-up Paths
The exact cost of some repairing paths cannot be calculated by the minimum-cost flow algorithm
  Down-and-up movement
  Back-and-forth movement
R1
R2
R3
R4
R5
R6
Source
Target
R1
R3
R2
R4
R6
R5
10
5
10
20
15
0
-10
should be
10
5
10
20
A
B
C
D
Notes: But, as one may concern that this has some corner cases that may fail in communication estimation caused by down-and-up or back-and-forth move.
Take this figure as an example, the original communication cost is 50.
And this is the repairing path with delta communication cost 5.
But after applying the remapping, we can see that the new communication cost is 75.
The delta communication cost actually is 25.

## Slide 17: Lemma of Topology Graph
The repairing path must subjects to conditions:
  Let be a given repairing path
  Let be the PE of the path at
R1
R2
R3
R4
R5
R6
Source
Target
R1
R2
R3
R4
R5
R6
Source
Target
Repairing path cannot have down-and-up or back-and-forth movement
We can proof that the overall is exactly the cost of MCF, if the repairing path has no down-and-up or back-and-forth movement

## Slide 18: Topology Graph Construction
Construct two topology graphs
  Right-up graph
  Right-down graph
Source
Target
R1
R2
R3
R4
R5
R6
R1
R2
R3
R4
R5
R6
Target
Source
R1
R3
R2
R4
R6
R5
10
5
10
20
A
B
C
D
Notes: Our third feature takes care this problem. This problem is caused by those down-and-up or back-and-forth move. We delete those undesired repairing paths by decomposing the topology graph.
By doing so, we can avoid the down-and-up or back-and-forth path and, thus, avoid the problem.
So, this is the topology graph we use for this case.

## Slide 19: A Complete Example
Obtain the repairing path with minimum overhead
  Repairing path: R1->R4->R5->R6
Target
R1
R2
R3
R4
R5
R6
R3
R6
0
15
20
-15
20
20
0
0
5
20
20
20
20
is
R1
R2
R4
R5
0
15
-10
25
20
-15
5
40
20
R1
R3
R2
R4
R6
R5
10
5
10
20
10
5
10
20
Source
A
B
C
D
Notes: This is the above example with all the communication costs on the edges.
In this case, we will find a repairing path from source, R1, R4, R5, R6 to target node. And, the delta communication cost is 5.
Again, the original communication cost is 50.
After applying this remapping, the new communication cost is 55.
Thus, the delta communication cost is 5 which is exactly the same as previously estimated.

## Slide 20: Outline
Multi-Processor System-on-Chip (MPSoC)
  Task remapping for fault-tolerant
Communication driven remapping method
  Model communication cost on edges
  Allow tasks be moved to non-neighboring PEs
Initial mapping improvement
Experimental results
Conclusions
Notes: Experimental results

## Slide 21: Initial Mapping Improvement
Our method can also be applied to improve the communication cost of a given initial mapping
Step1: Place a faulty PE Step2: Apply our repairing method Step3: Repeat Step1 and Step2 for iterations Step4: Select the mapping with lowest
Notes: The finally feature of our method is that it can also be applied to improve the communication cost of a given initial mapping.
Steps are shown on the slide.
First step: place a faulty PE
Step2: apply our repairing algorithm
And, repeat those steps for iterations
Finally, output the initial mapping with lowest communication cost.

## Slide 22: Outline
Multi-Processor System-on-Chip (MPSoC)
  Task remapping for fault-tolerant
Communication driven remapping method
  Model communication cost on edges
  Allow tasks be moved to non-neighboring PEs
Initial mapping improvement
Experimental results
Conclusions
Notes: Experimental results

## Slide 23: Initial Mapping Improvement
10.91% improvement on default mapping
4.16% improvement on NMAP [2]
Chart: Communication cost (avg. distance / byte)
| av_bench | RS_enc | RS_dec | H264-720p dec | H264-1080p dec | Fpppp | FFT-1024_complex | Sparse | Avg.
Default mapping | 1.5643 | 1.464 | 2.3018 | 2.2992 | 2.3017 | 2.1889 | 1.4903 | 1.72 | 1.9163
Default mapping + Ours | 1.0776 | 1.277 | 2.0592 | 2.0151 | 2.0161 | 2.1828 | 1.4903 | 1.54 | 1.7073
NMAP [2] | 1.1993 | 1.2698 | 2.1686 | 2.0797 | 2.0857 | 2.3141 | 1.4903 | 1.68 | 1.7859
NMAP + Ours | 1.1138 | 1.241 | 2.0828 | 1.992 | 1.9906 | 2.2232 | 1.4903 | 1.56 | 1.7117
10.91%
4.16%
Notes: For the repairing overhead, the communication cost of our method achieves 43.59% less on average than the previous work.

## Slide 24: Repairing Communication Overhead
43.59% less communication overhead on average
  Use a more precise communication cost model
Chart: Number of faulty PEs
| 0 | 1 | 2 | 3 | 4
Previous work [1] | 1.7859 | 1.9058 | 2.0201 | 2.1296 | 2.2347
Ours | 1.7859 | 1.8503 | 1.9108 | 1.9781 | 2.0673
43.59%
Notes: For the initial mapping, our method can improve the default mapping by 10.91% and improve the NMAP by 4.16%.

## Slide 25: Overall Effect
3.94% fewer overhead on initial mapping
39.08% less for remapping
Chart: Number of faulty PEs
| 0 | 1 | 2 | 3 | 4
Initial mapping: NMAP [2]; Repairing: previous work [1] | 1.7859 | 1.9058 | 2.0201 | 2.1296 | 2.2347
Initial mapping: NMAP+Ours; Repairing: previous work [1] | 1.7117 | 1.8262 | 1.9393 | 2.0477 | 2.1566
Initial mapping: NMAP+Ours; Repairing: Ours | 1.7117 | 1.781 | 1.8451 | 1.9134 | 1.9988
3.94%
39.08%
Notes: Lastly, the overall effect shows that our method provides 3.94% fewer overall communication overhead by the initial mapping improvement and further 39.08% less communication cost caused by fault-tolerant.

## Slide 26: Outline
Multi-Processor System-on-Chip (MPSoC)
  Task remapping for fault-tolerant
Communication driven remapping method
  Model communication cost on edges
  Allow tasks be moved to non-neighboring PEs
Initial mapping improvement
Experimental results
Conclusions
Notes: Conclusions

## Slide 27: Conclusions
A communication driven remapping algorithm
  Tolerate processing element failures
    Use precise communication cost model
    Allow flexible non-neighboring task movement
  Improve the initial mapping
  Be compared with previous work
    Higher repair rate
    Less communication overhead
      Initial mapping (4.16%)
      Remapping (43.59%)
Notes: We proposed a communication driven remapping algorithm to tolerate processing element failures. It provides a precise communication cost model and a flexible non-neighboring PE movement capability for tasks. Also, it can effectively improve the initial mapping. By the experimental results, it achieves 100% repair rate, improve initial mapping by 4.16%, and reduce 43.59% communication overhead.

## Slide 28: Thank you for listening

## Slide 29: Backup Slides

## Slide 30: Lemma of Topology Graph
B
………
…
…
………

## Slide 31: Cost of MCF Algorithm ()
B
………
…
…
………
………
…
…
………
B
Exactly the cost of the MCF algorithm

## Slide 32: Environment & Benchmarks
Transaction Generator (TG) [10]
NoC traffic benchmark suite MCSL [12]
Mesh architecture
Application | # Tasks | # Communication Links | 
 |  | Among tasks | Among PEs
av_bench [11] | 40 | 57 | 25
RS_enc | 262 | 348 | 18
RS_dec | 182 | 392 | 71
H264-720p_dec | 2311 | 3461 | 65
H264-1080p_dec | 5191 | 7781 | 65
Fpppp | 334 | 1145 | 120
FFT-1024_complex | 16384 | 25600 | 116
Sparse | 96 | 67 | 34