## Slide 1: Architectural Evaluations on TSV Redundancy for Reliability Enhancement
Logos are allowed on this page only!
Yen-Hao Chen, Chien-Pang Chiu, Russell Barnes, TingTing Hwang
Notes: Thank you for your introduction. This is the title I am going to present, “architectural evaluations on TSV redundancy for reliability enhancement”.

## Slide 2: Outline
TSV redundancy in 3D ICs
  Redundancy architectures
  Reliability metrics
Reliability evaluation flow
Architectural enhancements
Evaluation of redundant TSV architectures
  Reliability
  Area overhead
  Redundancy scheme selection
  Chip-level evaluation
Conclusions
Notes: This is the outline. First, we will talk about the TSV redundancy in 3D ICs including redundancy architectures and reliability metrics. And then, we will present the reliability evaluation flow. With the flow, we can do the architectural enhancements. Then, we will discuss the findings of the evaluation of redundant TSV architectures. And, finally, the conclusions.
Let’s start with the TSV redundancy in 3D ICs.

## Slide 3: Three-dimensional Integrated Circuits (3D ICs)
A solution to the interconnect bottleneck of CMOS scaling
  Signals can be transmitted vertically through TSVs
    Short interconnect paths
    High I/O density
    …, etc.
  But TSV reliability is a problem
    Cracks caused by manufactural defect
    Voids caused by aging effect
TSV
Void
Crack
Notes: 3D IC technique is said to be a solution to the interconnect bottleneck of CMOS scaling. In 3D IC, signals can be transmitted vertically through dies with TSVs. That comes with several advantages, for example, short interconnect paths and higher I/O density, etc. But, the TSV reliability is a problem.
For example, we may have cracks caused by the manufactural defect or voids caused by the aging effect.

## Slide 4: TSV Block
The manufactural yield can be improved by regular placement
  Avoid the manufactural defects by placing TSVs into TSV block
4x4 TSV block
8x8 TSV block
12x12 TSV block
Notes: The manufactural defect and be avoid by placing TSVs into block, that is the TSV block.
For example, we can have a 4x4 TSV block, an 8x8 TSV block, or a 12x12 TSV block.

## Slide 5: TSV Redundancy
Redundant TSVs are added for higher reliability
  For both manufactural and aging defects
4x4 TSV block
Redundant TSV
Redundant TSV
8x8 TSV block
12x12 TSV block
Redundant TSV
Notes: Also, we may add some redundant TSVs for higher reliability.
For example, we can have the redundant TSVs at the corners, or a row of redundant TSVs, or like this one.

## Slide 6: Redundant TSV Architectures
Several redundant TSV architectures have been proposed
Shift (4x4)
Switch (4x4)
Router (8x8)
Ring (8x8)
[TVLSI’12]
[JSSC’10]
[DATE’12]
[TVLSI’16]
Notes: Several redundant TSV architectures have been proposed including Shift, Switch, Router, and Ring.

## Slide 7: Shift Architecture [TVLSI’12]
One redundant TSV is added for each row
Single direction of row shifting is supported by MUX
  2-to-1 MUX
Pros: very low area cost
Cons: only single direction of row shifting
Shift (4x4)
Notes: For the Shift architecture, one redundant TSV is added for each row. The single direction of row shifting is supported by MUX.
Normally, the normal TSVs are used to transmit signals. When a faulty TSV occurred, the Shift architecture can reconfigure itself to transmit the signals.
The advantage of Shift is very low area cost, But the disadvantage of Shift is only single direction of row shifting.

## Slide 8: Switch Architecture [JSSC’10]
Two redundant TSVs are linked to two ends of each row
Dual direction of row shifting is supported by MUX
  3-to-1 MUX (or 2-to-1 MUX)
Pros: low area cost
Cons: only dual direction of row shifting
Switch (4x4)
Notes: For the Switch architecture, two redundant TSVs are linked to two ends of each row. The dual direction row shifting is supported by MUX.
Normally, the normal TSVs are used to transmit signals. When two faulty TSVs occurred, the Switch architecture can reconfigure itself to transmit the signals.
The advantage of Switch is low area cost, but the disadvantage is the only dual direction of row shifting.

## Slide 9: Router-based Architecture [DATE’12]
Two rows of redundant TSVs are added to the sides
Two dimensional shifting is supported by router
  Three 3-to-1 MUXes per router
Pros: very high repairing ability
Cons: very high area cost
Router (8x8)
Signal
TSV
Router
Signal
TSV
Router
Notes: For the Router-based architecture, there are two rows of redundant TSVs on the sides. Two dimensional shifting is supported by the router which contain three 3-to-1 MUXes per each.
Normally, the signal is transmitted by its nearest TSV through the router. When a faulty TSV occurred, the routers can shift the signal to the redundant TSV. Also, this is a valid configuration.
The advantage of the Router is high repairing ability, but the disadvantage is high area cost for routers.

## Slide 10: Ring-based Architecture [TVLSI’16]
4 redundant TSVs are located at corners
Two dimensional shifting is supported by MUX
  4-to-1 MUX (or 3-to-1 MUX, or 2-to-1 MUX)
Pros: flexible shifting directions
Cons: median area cost
Signal
TSV
Signal
TSV
Signal
TSV
Ring (8x8)
Notes: For the Ring-based architecture, 4 redundant TSVs are located at corners. Two dimensional shifting is supported by MUX.
Normally, signals are transmitted by its nearest TSV through the MUXes. When a faulty TSV occurred, the Ring can reconfigure itself to shift the signal to the redundant TSV. Also, this is a valid reconfiguration.
The advantage of the Ring is the flexible shifting directions, but the disadvantage is that the median area cost.

## Slide 11: Motivation
Various redundancy scheme with different reliability and cost
Do we always need the most expensive redundancy scheme for all TSV block sizes?
Chart: TSV BLOCK SIZE
| 4x4 | 8x8 | 12x12 | 16x16 | 20x20 | 24x24 | 28x28 | 32x32
Shift | 1.264 | 1.1413 | 1.1004 | 1.08 | 1.0677 | 1.0595 | 1.0537 | 1.0493
Switch | 1.5279 | 1.2826 | 1.2008 | 1.1599 | 1.1354 | 1.119 | 1.1073 | 1.0986
Router | 1.6117 | 1.3617 | 1.2784 | 1.2367 | 1.2117 | 1.1951 | 1.1831 | 1.1742
Ring-1 | 1.3644 | 1.1774 | 1.095 | 1.0855 | 1.0781 | 1.0653 | 1.0629 | 1.0608
Lower is better
The area overhead of Router is relatively high when small sizes
We would like to understand how the best redundant TSV architecture for different TSV block sizes differs with respect to the overhead and reliability.
Notes: Thus, we have various TSV block sizes with different reliability and cost. The figure shows the normalized area comparison on different architectures with various TSV block sizes.
As shown on the figure the area overhead in small blocks is relatively higher. With this observation, we came with a question: do we always need the most expensive scheme all the time?
We would like to understand how the best redundant TSV architecture for different TSV block sizes differs with respect to the overheads and reliability.

## Slide 12: Outline
TSV redundancy in 3D ICs
  Redundancy architectures
  Reliability metrics
Reliability evaluation flow
Architectural enhancements
Evaluation of redundant TSV architectures
  Reliability
  Area overhead
  Redundancy scheme selection
  Chip-level evaluation
Conclusions

## Slide 13: Mean-time-to-failure (MTTF)
A commonly used reliability metric
An average time of which a chip can perform in the field
Chart: TSV BLOCK SIZE
| 8x8 | 12x12 | 16x16 | 20x20 | 24x24 | 28x28 | 32x32
Shift | 4.7042 | 3.794 | 3.3288 | 3.0059 | 2.7686 | 2.5864 | 2.4032
Switch | 9.0472 | 4.9659 | 4.2708 | 3.9043 | 3.5857 | 3.4085 | 3.208
Router | 33.0764 | 9.4697 | 6.2845 | 5.5268 | 5.1208 | 4.8395 | 4.6285
Ring-1 | 9.2064 | 5.4063 | 4.769 | 4.4047 | 4.1484 | 3.9403 | 3.7977
Higher is better
Notes: The mean-time-to-failure is a commonly used reliability metric. It is an average time of which a chip can perform in the field. The figure shows the MTTF on different architectures with various TSV block sizes.

## Slide 14: New Reliability Metric Needed
MTTF does not present the yield rate under a target lifetime
Chart: MTTF (YEARS)
Chart: MTTF (YEARS)
Phone 1 (MTTF=5)
Phone 2 (MTTF=6)
Target lifetime
Better?
Actually, phone 1 is more reliable.
Lower is better
Notes: But, the MTTF does not present the yield rate under a target lifetime.
For example, there are two mobile phones, namely phone1 and phone2, with the mean-time-to failure 5 and 6, respectively. Does that mean the phone2 is better than phone1? Considering the lifetime of a mobile phone typically is no longer than three years, MTTF hardly represent the reliability of those mobile phones. For some cases, the variation of the phone2 may be higher, thus, actually, phone1 is more reliable than phone2.

## Slide 15: Proposed Reliability Metric: Repair Rate
We proposed another reliability metric, repair rate
  The probability that the chip can survive longer than a target lifetime
Chart: TSV BLOCK SIZE
| 4x4 | 8x8 | 12x12 | 16x16 | 20x20 | 24x24 | 28x28 | 32x32
Shift | 0.996 | 0.956 | 0.881 | 0.741 | 0.55 | 0.349 | 0.199 | 0.079
Switch | 1 | 0.998 | 0.992 | 0.974 | 0.951 | 0.895 | 0.836 | 0.726
Router | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Ring-1 | 1 | 1 | 0.999 | 0.998 | 0.999 | 1 | 0.991 | 0.994
3-year target lifetime
Higher is better
Notes: Thus, we proposed another reliability metric, repair rate, which is the probability that the chip can survive longer than a target lifetime. This figure shows the repair rate on different architectures with various TSV block sizes.
Recall that the mean-time-to-failure of the Shift architecture when size equals to 16x16x is over three years. But actually, the repair rate with 3-year target lifetime is below 80%, which is quiet very low.

## Slide 16: Outline
TSV redundancy in 3D ICs
  Redundancy architectures
  Reliability metrics
Reliability evaluation flow
Architectural enhancements
Evaluation of redundant TSV architectures
  Reliability
  Area overhead
  Redundancy scheme selection
  Chip-level evaluation
Conclusions
Notes: Now we are going to discuss the reliability evaluation flow for the repair rate.

## Slide 17: Reliability Evaluation Flow
Maximum flow & path check
Time > target lifetime
Case pass
Case fail
Yes
No
Pass
Fail
Generate TSV fault patterns
Time = Time + 1
Time = 0
Has negative slack path
Flow == # of signal TSVs
Fail
Pass
No
Yes
Yes
No
Maximum flow algorithm
Update graph
Construct graph
Notes: This is the reliability evaluation flow diagram.

## Slide 18: Reliability Evaluation Flow (Top)
Evaluate the lifetime of a chip
  Loop until target lifetime
Maximum flow & path check
Time > target lifetime
Case pass
Case fail
Yes
No
Pass
Fail
Generate TSV fault patterns
Time = Time + 1
Time = 0
Notes: Let start with the first part. It is the evaluation of the lifetime of a chip. It loops until the target lifetime.
At the beginning, we set the time to zero and enter the loop. Check whether the time is larger than the target lifetime. If not, we generate the TSV fault pattern, perform the maximum flow and path check step. If fail, the case failed. If pass, we advance the time, and recheck the looping condition again. Until the time is larger than the target lifetime.

## Slide 19: Maximum Flow & Path Check
Has negative slack path?
Flow == number of signals
Fail
Pass
No
Yes
Yes
No
Maximum flow algorithm
Update graph
Construct graph
Decide if there is a valid reconfiguration
  Under the given fault pattern
Notes: For the maximum flow and path check. This step decides if there is a valid reconfiguration under the given fault pattern.
First, we construct the graph and apply the maximum flow algorithm. Then, we check if the flow number is equal to the number of signals. If no, then, the it fails. If yes, we further check if it has negative slack paths? If no, then it passes. Otherwise, we will update the graph by removing those unwanted paths. And redo the maximum flow again.

## Slide 20: Reliability Evaluation Flow
Maximum flow & path check
Time > target lifetime
Case pass
Case fail
Yes
No
Pass
Fail
Generate TSV fault patterns
Time = Time + 1
Time = 0
Has negative slack path
Flow == # of signal TSVs
Fail
Pass
No
Yes
Yes
No
Maximum flow algorithm
Update graph
Construct graph
Notes: Again this is the reliability evaluation flow diagram.

## Slide 21: Outline
TSV redundancy in 3D ICs
  Redundancy architectures
  Reliability metrics
Reliability evaluation flow
Architectural enhancements
Evaluation of redundant TSV architectures
  Reliability
  Area overhead
  Redundancy scheme selection
  Chip-level evaluation
Conclusions
Notes: With the flow, we now can do the architectural enhancements.

## Slide 22: Ring-based Architecture [TVLSI’16]
More flexible and cost-efficient than the others
  E.g.: a Ring 8x8 TSV block
    4 redundant TSVs located at corners
    3 inner rings
      Single direction of ring shifting
      Outer neighbor shifting
    An outermost ring
      Dual direction of ring shifting
      Inner neighbor shifting
Redundant TSV
Inner ring
Outermost ring
Notes: We start with a ring-based architecture, because it is more flexible and cost-efficient than the others. Take this 8x8 Ring as an example. It has four redundant TSVs located at corners. There are four rings including three inner ring and one outermost ring. For the inner rings, signals can do the single direction ring shifting. For the outermost ring, signals can do the dual direction ring shifting. For the inner rings, signals can do the outer neighbor ring shifting. For the outermost ring, signals can do the inner neighbor ring shifting.

## Slide 23: Enhancements
Increase the number of redundant TSVs to improve reliability
Remove non-efficient shifting MUXes to reduce area overhead
  Outermost ring
  Inner rings
Notes: We are going to do some enhancements on the ring architecture. First, we increase the number of redundant TSVs on the outermost ring to improve reliability. And then, we remove non-efficient shifting MUXes to reduce area overhead including the outermost ring and the inner rings.

## Slide 24: Number of Redundant TSVs
: # of TSVs between two redundant TSVs
  Margin-[]
margin-4
Chart: TSV BLOCK SIZE
| 4x4 | 8x8 | 12x12 | 16x16 | 20x20 | 24x24 | 28x28 | 32x32
margin-5 | 1 | 1 | 0.999 | 0.998 | 0.999 | 1 | 0.991 | 0.994
margin-6 | 1 | 0.997 | 0.999 | 0.998 | 0.994 | 1 | 0.948 | 0.946
margin-7 | 1 | 0.997 | 1 | 0.987 | 0.995 | 0.952 | 0.948 | 0.731
Because margin-6 starts to decrease rapidly, we choose margin-5 for the following experiments.
Higher is better
Notes: First, we increase the number of redundant TSVs on the outermost ring. We define a new variable RTS_margin which is the number of TSVs between two redundant TSVs. Take RTS_marign equals to 4 as an example. The number of TSVs between any two redundant TSVs should not larger than 5, so we have to add some more redundant TSVs shown on the figure. We call this architecture margin-4.
And, this figure shows the repair rate comparison on the margin-5, margin-6, and margin-7 with various TSV block sizes.
Because marign-6 starts to decrease rapidly, we choose margin-5 for the following experiments.

## Slide 25: Outermost Ring MUX-area Reduction
Originally, outermost ring was connected to the inner neighbor
  Support inner neighbor shifting
With connections
Chart: tsv block SIZE
| 4x4 | 8x8 | 12x12 | 16x16 | 20x20 | 24x24 | 28x28 | 32x32
with connections | 1 | 1 | 0.999 | 0.998 | 0.999 | 1 | 0.991 | 0.994
without connections | 1 | 1 | 0.999 | 0.998 | 0.999 | 1 | 0.991 | 0.994
Without connections
Higher is better
Repair rates w/ or w/o connections to inner neighbor are the same. Thus, the connections are removed in the following experiments.
Notes: For the outermost ring MUX-area reduction. Originally, outermost ring was able to shift to the inner ring to allow all rings to be able to shift to another ring. We want to know whether this design is efficient. This figure shows the repair rate on the Ring architecture with and without the outermost ring connects to the inner ring. The figure shows that the repair rate with and without outermost ring connections to inner neighbor are the same. Thus, the connections are removed in the following experiments.

## Slide 26: Inner Rings MUX-area Reduction
Chart: TSV BLOCK SIZE
| 4x4 | 8x8 | 12x12 | 16x16 | 20x20 | 24x24 | 28x28 | 32x32
share-1 | 1 | 1 | 0.999 | 0.998 | 0.999 | 1 | 0.991 | 0.994
share-2 | 1 | 0.998 | 0.983 | 0.982 | 0.96 | 0.945 | 0.932 | 0.894
share-3 | 1 | 0.996 | 0.981 | 0.97 | 0.932 | 0.903 | 0.861 | 0.811
: # of TSVs share a MUX to shift to outer neighbor
  Share-[], Ring-[]
Share-1
Share-2
(Ring-1)
(Ring-2)
(Ring-1)
(Ring-2)
Because share-3 starts to decrease rapidly, we use share-1 & share-2 for the following evaluation.
Higher is better
Because share-3 starts to decrease rapidly, we use share-1 (Ring-1) & share-2 (Ring-2) for the following evaluation.
Notes: Finally, for the inner rings MUX-area reduction. We defined another variable, num_share which means the number of TSVs share a MUX to shift to outer ring. For example, share-1 means not reduction. And, share-2 means two TSVs share a MUX to shift to outer ring. This is the repair rate comparison on share-1, share-2, and share-3 with various TSV block sizes. Because share-3 starts to decrease rapidly, we use share-1 and share-2 for the following experiments. And, we are going to name the share-1 and share-2, ring-1 and ring-2, respectively.

## Slide 27: Outline
TSV redundancy in 3D ICs
  Redundancy architectures
  Reliability metrics
Reliability evaluation flow
Architectural enhancements
Evaluation of redundant TSV architectures
  Reliability
  Area overhead
  Redundancy scheme selection
  Chip-level evaluation
Conclusions
Notes: Now, we are going to talk about our evaluation findings, including reliability, area overhead, selection of redundancy scheme, and chip-level evaluation. Let’s start with the reliability.

## Slide 28: Repair Rates with 3-year Target Lifetime
All redundancy schemes are effective when size = 4x4
Repair rates of Switch and Ring-2 decrease when size > 20x20
Ring-1 and Router achieve 99% repair rates with every sizes
Chart: tsv block size
| 4x4 | 8x8 | 12x12 | 16x16 | 20x20 | 24x24 | 28x28 | 32x32
None | 0.795 | 0.412 | 0.133 | 0.04 | 0.006 | 0.001 | 0 | 0
Shift | 0.996 | 0.956 | 0.881 | 0.741 | 0.55 | 0.349 | 0.199 | 0.079
Switch | 1 | 0.998 | 0.992 | 0.974 | 0.951 | 0.895 | 0.836 | 0.726
Router | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Ring-1 | 1 | 1 | 0.999 | 0.998 | 0.999 | 1 | 0.991 | 0.994
Ring-2 | 1 | 0.998 | 0.983 | 0.982 | 0.96 | 0.945 | 0.932 | 0.894
Higher is better
Notes: This is the repair rates with 3-year target lifetime on different architectures with various TSV block sizes. It shows that the repair rate of Switch and Ring-2 decrease when size is larger than 20x20. And Ring-1 and router achieve 99% repair rates with every sizes.

## Slide 29: Outline
TSV redundancy in 3D ICs
  Redundancy architectures
  Reliability metrics
Reliability evaluation flow
Architectural enhancements
Evaluation of redundant TSV architectures
  Reliability
  Area overhead
  Redundancy scheme selection
  Chip-level evaluation
Conclusions
Notes: For the area overhead.

## Slide 30: Area Overhead
Redundant TSV overhead
  Repairing ability
MUX-area overhead
  Signal shifting
Shift (4x4)
Ring (4x4)
Switch (4x4)
Router (4x4)

## Slide 31: Redundant TSV Overhead
Switch and Router have the highest redundant TSV overhead
Shift has the lowest redundant TSV overhead with size < 8x8
Ring-1 and Ring-2 have the lowest overhead for size > 12x12
Chart: tsv block size
| 4x4 | 8x8 | 12x12 | 16x16 | 20x20 | 24x24 | 28x28 | 32x32
Shift | 0.25 | 0.125 | 0.083333 | 0.0625 | 0.05 | 0.041667 | 0.035714 | 0.03125
Switch | 0.5 | 0.25 | 0.16667 | 0.125 | 0.1 | 0.083333 | 0.071429 | 0.0625
Router | 0.5 | 0.25 | 0.16667 | 0.125 | 0.1 | 0.083333 | 0.071429 | 0.0625
Ring-1 | 0.33333 | 0.14286 | 0.058824 | 0.04918 | 0.041667 | 0.028571 | 0.026178 | 0.024
Ring-2 | 0.33333 | 0.14286 | 0.058824 | 0.04918 | 0.041667 | 0.028571 | 0.026178 | 0.024
Shift (4x4)
Ring (4x4)
Switch (4x4)
Router (4x4)
Lower is better
Notes: This figure shows the ratio of redundant TSVs and signals. By the figure, Siwtch and Router have the highest ratio, meanwhile, the ratio of Ring is lower than Shift architecture when the size is larger than 12x12.

## Slide 32: MUX-area Overhead
Chart: tsv block size
| 4x4 | 8x8 | 12x12 | 16x16 | 20x20 | 24x24 | 28x28 | 32x32
Shift | 1.3965 | 1.6293 | 1.7068 | 1.7456 | 1.7689 | 1.7844 | 1.7955 | 1.8038
Switch | 2.793 | 3.2585 | 3.4137 | 3.4912 | 3.5378 | 3.5688 | 3.591 | 3.6076
Router | 11.172 | 11.172 | 11.172 | 11.172 | 11.172 | 11.172 | 11.172 | 11.172
Ring-1 | 3.1033 | 3.458 | 3.6145 | 3.6324 | 3.6464 | 3.6708 | 3.6753 | 3.6793
Ring-2 | 3.1033 | 3.059 | 3.0668 | 2.9914 | 2.9482 | 2.9393 | 2.9149 | 2.8973
Router has higher MUX-area than others
Switch and Ring-1 have almost the same MUX-area
Ring-2 is an obvious reduction compared to Ring-1
Shift has the lowest MUX-area overhead
Lower is better
Notes: This is the MUX-area overhead on different architectures with various TSV block sizes. It shows that Router has higher MUX-area than others, because a router consists of three 3-to-1 MUXes. And, Switch and Ring-1 have almost the same MUX-area. Also, Ring-2 is an obvious reduction compared to Ring-1. Lastly, Shift has the lowest MUX-area, because it uses only 2-to-1 MUXes.

## Slide 33: Overall Area Overhead
Router has the highest area overhead
Switch shows the median area overhead
Ring-1, Ring-2, and Shift have the lowest area overhead
Chart: tsv block size
| 4x4 | 8x8 | 12x12 | 16x16 | 20x20 | 24x24 | 28x28 | 32x32
Shift | 1.264 | 1.1413 | 1.1004 | 1.08 | 1.0677 | 1.0595 | 1.0537 | 1.0493
Switch | 1.5279 | 1.2826 | 1.2008 | 1.1599 | 1.1354 | 1.119 | 1.1073 | 1.0986
Router | 1.6117 | 1.3617 | 1.2784 | 1.2367 | 1.2117 | 1.1951 | 1.1831 | 1.1742
Ring-1 | 1.3644 | 1.1774 | 1.095 | 1.0855 | 1.0781 | 1.0653 | 1.0629 | 1.0608
Ring-2 | 1.3644 | 1.1734 | 1.0895 | 1.0791 | 1.0711 | 1.058 | 1.0553 | 1.053
Lower is better
Notes: This figure shows the overall area overhead on different architectures with various TSV block sizes. By the figure, the Router has the highest area overhead and is followed by Switch, Ring-1, and Ring-2. Also, the Shift architecture has the lowest area overhead.

## Slide 34: Outline
TSV redundancy in 3D ICs
  Redundancy architectures
  Reliability metrics
Reliability evaluation flow
Architectural enhancements
Evaluation of redundant TSV architectures
  Reliability
  Area overhead
  Redundancy scheme selection
  Chip-level evaluation
Conclusions
Notes: Selection of redundancy scheme.

## Slide 35: Redundancy Scheme Selection
We like to find the most cost-efficient and reliable scheme
  Achieves the target repair rate and has the lowest area overhead
Chart: tsv block size
| 4x4 | 8x8 | 12x12 | 16x16 | 20x20 | 24x24 | 28x28 | 32x32
Shift | 1.264 | 1.1413 | 1.1004 | 1.08 | 1.0677 | 1.0595 | 1.0537 | 1.0493
Switch | 1.5279 | 1.2826 | 1.2008 | 1.1599 | 1.1354 | 1.119 | 1.1073 | 1.0986
Router | 1.6117 | 1.3617 | 1.2784 | 1.2367 | 1.2117 | 1.1951 | 1.1831 | 1.1742
Ring-1 | 1.3644 | 1.1774 | 1.095 | 1.0855 | 1.0781 | 1.0653 | 1.0629 | 1.0608
Ring-2 | 1.3644 | 1.1734 | 1.0895 | 1.0791 | 1.0711 | 1.058 | 1.0553 | 1.053
Chart: tsv block size
| 4x4 | 8x8 | 12x12 | 16x16 | 20x20 | 24x24 | 28x28 | 32x32
None | 0.795 | 0.412 | 0.133 | 0.04 | 0.006 | 0.001 | 0 | 0
Shift | 0.996 | 0.956 | 0.881 | 0.741 | 0.55 | 0.349 | 0.199 | 0.079
Switch | 1 | 0.998 | 0.992 | 0.974 | 0.951 | 0.895 | 0.836 | 0.726
Router | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Ring-1 | 1 | 1 | 0.999 | 0.998 | 0.999 | 1 | 0.991 | 0.994
Ring-2 | 1 | 0.998 | 0.983 | 0.982 | 0.96 | 0.945 | 0.932 | 0.894
99%
Lower is better
Higher is better
Notes: With the above evaluation, we are going to discuss how to selection a redundancy TSV architecture. We like to know the lowest area overhead cost of all of the architectures that achieves the target repair rate. For example, let’s say we want a 99% repair rate under 3-year target lifetime.

## Slide 36: 99% Repair Rate with 3-year Target Lifetime
Shift is the best choice in terms of area overhead for size = 4x4
Ring-2 is the most cost-efficient choice when size = 8x8
Ring-1 reaches the rate and requires less area when size > 12x12
Chart: tsv block size
| 4x4 | 8x8 | 12x12 | 16x16 | 20x20 | 24x24 | 28x28 | 32x32
Shift | 1.264
Switch | 1.5279 | 1.2826 | 1.2008
Router | 1.6117 | 1.3617 | 1.2784 | 1.2367 | 1.2117 | 1.1951 | 1.1831 | 1.1742
Ring-1 | 1.3644 | 1.1774 | 1.095 | 1.0855 | 1.0781 | 1.0653 | 1.0629 | 1.0608
Ring-2 | 1.3644 | 1.1734
Lower is better
Notes: We can reprint the area overhead figure shown on the slide. The missing segments mean that the architectures are not reliable under the TSV block sizes. The figure shows that the Shift architecture is the best choice in terms of area overhead for size equals to 4x4. And, Ring-2 is the most cost-efficient choice when size equals to 8x8. Meanwhile, Ring-1 reaches the repair rate and requires less area with size larger than 12x12.

## Slide 37: Outline
TSV redundancy in 3D ICs
  Redundancy architectures
  Reliability metrics
Reliability evaluation flow
Architectural enhancements
Evaluation of redundant TSV architectures
  Reliability
  Area overhead
  Redundancy scheme selection
  Chip-level evaluation
Conclusions
Notes: Chip-level evaluation

## Slide 38: Chip-level Evaluation
Number of TSV blocks depends on selection of TSV block size
  For a design with 120 signals to be transmitted through TSVs
    8 4x4 TSV blocks
    2 8x8 TSV blocks
2 8x8 TSV blocks
We like to know how it differs for different selections of TSV block sizes.
8 4x4 TSV blocks
Notes: The number of TSV blocks in a design depends on the selection of TSV block size. For example, given a design with 120 signals to be transmitted through the TSVs, we can choose 7 4x4 TSV blocks or 2 8x8 TSV blocks.
And, we like to know how it differs for different selections of TSV block sizes.

## Slide 39: Chip-level Results (Ring-2)
Higher repair rate when using smaller TSV block sizes
Less area overhead when using larger TSV block sizes
Chart: number of signals on design
| 512 | 1024 | 1536 | 2048 | 2560 | 3072
4x4 TSV block | 1.375 | 1.375 | 1.3644 | 1.367 | 1.3686 | 1.3644
8x8 TSV block | 1.2835 | 1.2193 | 1.1979 | 1.1872 | 1.1808 | 1.1765
12x12 TSV block | 1.1576 | 1.1576 | 1.1576 | 1.1576 | 1.0997 | 1.1094
Chart: number of signals on design
| 512 | 1024 | 1536 | 2048 | 2560 | 3072
4x4 TSV block | 1 | 1 | 1 | 1 | 1 | 1
8x8 TSV block | 0.98018 | 0.96268 | 0.94549 | 0.9286 | 0.91202 | 0.89573
12x12 TSV block | 0.93371 | 0.87182 | 0.81403 | 0.76007 | 0.72197 | 0.67411
Higher is better
Lower is better
The best choice depends on the reliability requirement. With the requirement (target repair rate), we can choose the most cost-efficient TSV block size.
Notes: This is the chip-level results. The left hand side figure is the repair rate comparison on various TSV block sizes with different number of signals in the design. It shows that smaller TSV block sizes are more reliable. And, the right hand side figure is the area comparison on various TSV block sizes with different number of signals in the design. It shows that larger TSV block sizes are more cost-efficient.
The best choice depends on the reliability requirement. With the requirement, that is the target repair rate, we can choose the most cost-efficient TSV block size.

## Slide 40: Outline
TSV redundancy in 3D ICs
  Redundancy architectures
  Reliability metrics
Reliability evaluation flow
Architectural enhancements
Evaluation of redundant TSV architectures
  Reliability
  Area overhead
  Redundancy scheme selection
  Chip-level evaluation
Conclusions
Notes: Conclusions

## Slide 41: Conclusions
We introduce a new measurement, repair rate, to compare the reliability of redundant TSV architectures
We also enhance the ring-based design to maintain a high repair rate with lower area overhead
Lastly, we evaluate several redundant TSV architectures for selecting the most suitable scheme when given a TSV block size in terms of repair rate and area overhead
Notes: We introduce a new measurement, repair rate, to compare the reliability of redundant TSV architectures. We also enhance the ring-based design to maintain a high repair rate with lower area overhead. Lastly, we evaluate several redundant TSV architectures for selecting the most suitable scheme when given a TSV block size in terms of repair rate and area overhead.

## Slide 42: Thank you for listening
Notes: This is my presentation. Thank you for listening.