## Slide 1: A Dynamic Link-latency Aware Cache Replacement Policy (DLRP)
Yen-Hao Chen, Allen C.-H. Wu, and TingTing Hwang
Department of Computer Science
National Tsing Hua University, Taiwan

## Slide 2: Summary
Non-uniform cache architecture (NUCA) has varied cache access latency
Access patterns with long dynamic latency show hit rate degradation due to the varied latency
  Hardware efficient online identification mechanism
  Dynamic link-latency aware cache replacement policy (DLRP)
The DLRP outperforms LRU by 53% for those access patterns with long dynamic latency

## Slide 3: Outline
Non-uniform cache architecture (NUCA)
  Varied latency related to bank location
Access pattern with long dynamic latency
  Identification mechanism
Dynamic link-latency aware cache replacement policy (DLRP)
  Replacement policy bit priority
Experimental results
Conclusions

## Slide 4: Non-uniform Cache Architecture
Partition a large cache into several banks
  Provide varied access latencies to banks
  Avoid a fixed worst-case access latency
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Core3
Private L1 cache
Shared L2 cache ( bank3 )
3
Shared L2 NUCA

## Slide 5: Varied Latency
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Core3
Private L1 cache
Shared L2 cache ( bank3 )
3
NUCA features varied latencies to different banks
Source
0
3
15
Latencies:
Core0
Private L1 cache
Shared L2 cache ( bank0 )
0
Core15
Private L1 cache
Shared L2 cache ( bank15 )
15
NUCA

## Slide 6: Latency & Cache Performance
Long latency blocks may have more interleaves
  More likely be evicted
a
a
Re-accessing
a
Re-accessing
a
Other applications
Long latency
Short latency
More likely being evicted

## Slide 7: Latency & Hit Rate
Many previous work on minimizing latency
  Data migration
  Cache partitioning
  Data duplication
But we found that the latency not always affect cache hit rate

## Slide 8: Bank Interleaved Access Pattern
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Core3
Private L1 cache
Shared L2 cache ( bank3 )
3
Time interval before re-accessing is the same
0
1
2
3
…
0
1
2
3
…
0
1
2
3
…
0
1
2
3
…
Source
Latency does not affect the cache hit rate

## Slide 9: Access Pattern Affected by Latency
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Core3
Private L1 cache
Shared L2 cache ( bank3 )
3
Always access same cache bank several times before accessing another cache bank
Source
Latency may affect the cache hit rate
a
…
a
…
a
…
a
…
b
…
b
Access Pattern with Long Dynamic Latency

## Slide 10: Motivation
Chart: Cache bank hit rate
| Bank0 | Bank5 | Bank10 | Bank15
No long dynamic latency | 0.96312 | 0.96248 | 0.96325 | 0.96342
With long dynamic latency | 0.96526 | 0.95033 | 0 | 0
Accessing pattern without long dynamic latency
  A similar cache hit rate across cache banks
Accessing pattern with long dynamic latency
  Low cache hit rate on cache bank far from core
Long latency
Short latency
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
NUCA
Source
We want to tackle the performance degradation issue on banks far from core for access patterns with long dynamic latency

## Slide 11: Outline
Non-uniform cache architecture (NUCA)
  Varied latency related to bank location
Access pattern with long dynamic latency
  Identification mechanism
Dynamic link-latency aware cache replacement policy (DLRP)
  Replacement policy bit priority
Experimental results
Conclusions

## Slide 12: Long Dynamic Latency
Static latency
  Average latency of all accesses
Dynamic latency
  Latency in a period
0
1
2
3
…
0
1
2
3
…
0
1
2
3
…
0
1
2
3
…
No long dynamic latency
With long dynamic latency
0
…
0
…
0
…
0
…
15
15
15
15
…
15
15
Long dynamic latency

## Slide 13: Identification Mechanism
Exponentially weighted moving average (EWMA)
If , a long dynamic latency
  Mean of average latency and maximum latency
0
1
2
3
…
0
1
2
3
…
0
1
2
3
…
0
1
2
3
…
No long dynamic latency
With long dynamic latency
0
…
0
…
0
…
0
…
15
15
15
15
…
15
15
Long dynamic latency

## Slide 14: Outline
Non-uniform cache architecture (NUCA)
  Varied latency related to bank location
Access pattern with long dynamic latency
  Identification mechanism
Dynamic link-latency aware cache replacement policy (DLRP)
  Replacement policy bit priority
Experimental results
Conclusions

## Slide 15: Cache Replacement Policy
Maintain priorities of cache blocks
A block with eviction priority is the victim
  E.g. SRRIP [1] gives () to new blocks
Eviction priority
High priority
Low priority
()
()
()
Smaller value mean higher priority (Evict the largest one)
Access
Access
Victim
[1] A. Jaleel, K. B. Theobald, S. C. S. Jr., and J. S. Emer, “High performance cache replacement using re-reference interval prediction (RRIP),” ISCA 2010
We want to give higher priorities to long latency data blocks
8-way cache set
Chart: Cache bank hit rate
| Bank0 | Bank5 | Bank10 | Bank15
No long dynamic latency | 0.96312 | 0.96248 | 0.96325 | 0.96342
With long dynamic latency | 0.96526 | 0.95033 | 0 | 0
Far from core
Near to core

## Slide 16: Dynamic Link-latency Aware Cache Replacement Policy (DLRP)
Compensate link-latency effect
  Give a higher priority to long latency data blocks
    i.e. giving () to new blocks
Eviction priority
High priority
Low priority
()
()
()
Smaller value mean higher priority (Evict the largest one)
Access
()
Access
Short latency
Access
Access
Long latency
8-way cache set
Victim
We want to give higher priorities to long latency data blocks
Chart: Cache bank hit rate
| Bank0 | Bank5 | Bank10 | Bank15
No long dynamic latency | 0.96312 | 0.96248 | 0.96325 | 0.96342
With long dynamic latency | 0.96526 | 0.95033 | 0 | 0
Far from core
Near to core

## Slide 17
Additional interleaved blocks caused by latency
a
a
a
a
Long distance
Short distance
: number of interleaved blocks from other applications
: number of interleaved blocks from the same application
: elapsed cycles between two accesses to same block

## Slide 18: Outline
Non-uniform cache architecture (NUCA)
  Varied latency related to bank location
Access pattern with long dynamic latency
  Identification mechanism
Dynamic link-latency aware cache replacement policy (DLRP)
  Replacement policy bit priority
Experimental results
Conclusions

## Slide 19: Benchmarking Kernels
The kernels are selected from various area
Name | Description | L1 MPKI
strcpy | String copy in standard library | 3.47
random | Random memory access | 55.56
mco | Matrix multiplication chain order | 0.00
hwdec | Haar wavelet image decompression | 18.46
rlchky | Right-looking Cholesky factorization | 36.39
2DConv | Two-dimensional discrete convolution | 79.91
llchky | Left-looking Cholesky factorization | 3.17
hwcom | Haar wavelet image compression | 18.46
multiply | Matrix multiplication | 63.01
transpose | Matrix transposition | 81.56

## Slide 20: Experimental Results
Kernel | Identification mechanism (With long dynamic latency?) | IPC (normalized to LRU) |  | 
 |  | NRU | SRRIP | DLRP
strcpy | No | 1.00 | 1.00 | 1.00
random | No | 1.00 | 1.00 | 1.00
mco | No | 1.00 | 1.00 | 1.00
hwdec | No | 1.00 | 1.00 | 1.00
rlchky | No | 0.98 | 0.99 | 0.99
Avg. | No | 0.99 | 1.00 | 1.00
llchky | Yes | 1.00 | 1.00 | 1.03
2DConv | Yes | 1.08 | 1.15 | 1.73
hwcom | Yes | 1.00 | 1.32 | 1.38
multiply | Yes | 1.17 | 1.48 | 1.75
transpose | Yes | 1.16 | 1.51 | 1.78
Avg. | Yes | 1.08 | 1.29 | 1.53
Multi-application
(0.00)
(0.24)
(0.45)
No long dynamic latency
With long dynamic latency

## Slide 21: Cache Performance Degradation
DLRP retain hit rate on long physical distances for access pattern with long dynamic latency
Far from core
Near to core
Chart: Link-latency between core and its data locations
| 0 | 1 | 2 | 3 | 4 | 5 | 6
Unaware of dynamic latency (SRRIP) | 0.87062 | 0.85726 | 0.84104 | 0.80712 | 0.71699 | 0.61726 | 0.37143
Aware of dynamic latency (DLRP) | 0.88052 | 0.88331 | 0.87633 | 0.87186 | 0.87894 | 0.87896 | 0.88648

## Slide 22: Mixed Kernels
Better perf. on kernels with long dynamic latency
  Relatively small performance impact on others
Workload | Memory-intensive |  | Compute-intensive (CI) (MPKI=0.00)
 | With long dynamic latency (DL) | No long dynamic latency (NDL) | 
1DL, 3NDL, 12CI | 1.05 | 1.00 | 1.00
1DL, 4NDL, 11CI | 1.14 | 1.00 | 1.00
1DL, 5NDL, 10CI | 1.29 | 0.99 | 1.00
1DL, 6NDL, 9CI | 1.37 | 0.99 | 1.00
1DL, 7NDL, 8CI | 1.53 | 0.99 | 1.00
1DL, 8NDL, 7CI | 1.54 | 0.99 | 1.00
Massive improvement
Small impact

## Slide 23: Outline
Non-uniform cache architecture (NUCA)
  Varied latency related to bank location
Access pattern with long dynamic latency
  Identification mechanism
Dynamic link-latency aware cache replacement policy (DLRP)
  Replacement policy bit priority
Experimental results
Conclusions

## Slide 24: Conclusions
Non-uniform cache architecture (NUCA) has varied cache access latency
Access patterns with long dynamic latency show hit rate degradation due to the varied latency
  Hardware efficient online identification mechanism
  Dynamic link-latency aware cache replacement policy (DLRP)
The DLRP outperforms LRU by 53% for those access patterns with long dynamic latency

## Slide 25: Thank you for listening

## Slide 26: Backup Slides

## Slide 27: Definition
Accessing pattern with long dynamic latency
  if recently accessing blocks are mostly with the same distance
Variance of physical distances
  Average of physical distances
0
1
2
3
…
0
1
2
3
…
0
1
2
3
…
0
1
2
3
…
Non-distance-sensitive accessing pattern
Distance-sensitive accessing pattern
0
…
0
…
0
…
0
…
15
15
15
15
…
15
15
Large variance
Small variance

## Slide 28: Identification Mechanism
0
1
2
3
…
0
1
2
3
…
0
1
2
3
…
0
1
2
3
…
Non-distance-sensitive accessing pattern
Distance-sensitive accessing pattern
0
…
0
…
0
…
0
…
15
15
15
15
…
15
15
An efficient online hardware monitor is proposed
  Exponentially weighted moving average (EWMA)
Constant EWMA
Varied EWMA

## Slide 29: Definition and Identification
Both variance and EWMA can differentiate
  Non-distance-sensitive accessing pattern
  Distance-sensitive accessing pattern
Variance is good for mathematical description
EWMA is easy for hardware implementation
  Low area and energy overheads
Accessing pattern | Variance | EWMA
Non-distance-sensitive | Large | Constant
Distance-sensitive | Small | Varied
Accessing pattern |  | EWMA
Non-distance-sensitive | Large | Constant
Distance-sensitive | Small | Varied

## Slide 30: DARP Top-level RPB Selection
Non-distance-sensitive accessing pattern
  Behave same as conventional policy [1]
    Set RPB to 0 on hit
    Set RPB to on miss
  is don’t care
Distance-sensitive accessing pattern
    Set RPB to 0 on hit
    Set RPB to on miss
0 1
0 1
Sub
0
Replacement policy bits (RPB)
Miss?
Distance-sensitive accessing pattern?
[1] A. Jaleel, K. B. Theobald, S. C. S. Jr., and J. S. Emer, “High performance cache replacement using re-reference interval prediction (RRIP),” ISCA 2010

## Slide 31
Additional interleaved blocks caused by distance
a
a
a
a
Long distance
Short distance
: number of interleaved blocks from other applications
: number of interleaved blocks from the same application
: eclipsed cycles between two accesses to same block

## Slide 32: Re-reference Interval (RRI) [1]
[1] A. Jaleel, K. B. Theobald, S. C. S. Jr., and J. S. Emer, “High performance cache replacement using re-reference interval prediction (RRIP),” ISCA 2010
Number of blocks accessed before re-accessing
Larger RRI is more likely being evicted
  RRI from other applications
  RRI from the same application
a
a
From the same application
From other applications
Accessed blocks before re-accessing
Re-accessing
A 16-way cache will be enough to cover all blocks

## Slide 33: Hardware Monitor
Each bank has separated monitors for each core
  Obtain , ,
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Core3
Private L1 cache
Shared L2 cache ( bank3 )
3
Mon. 0
Mon. 1
…
Mon.15
Additional hardware
Monitoring address
tag
index
tag0
tag1
tag15
…
Interval addresses
Monitor
Timestamp
v
v
v
v
08:30:25
2
3
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Core3
Private L1 cache
Shared L2 cache ( bank3 )
3

## Slide 34: Operation of Hardware Monitor
Sampled address as representation of the pattern
  Reduce monitoring overhead
  Enough to capture by exp.
a
a
From the same application
From other applications
Accessed blocks before re-accessing
Monitoring address
Interval addresses
Monitor
Timestamp
a
0
0
08:30:25
Re-accessing
Monitoring address
1
2
1
2
3
tag
index
tag0
tag1
tag15
…
v
v
v
v
Report , ,

## Slide 35: Control Flow of Hardware Monitor
When a cache accessing request issued
  Request information will be passed to monitor
Cache access from core to address in monitor of core
==
Do nothing
+1
Yes
Yes
Yes
No
No
No
== monitoring address
interval addresses
Update interval address
Report , , and
Reset monitor

## Slide 36: Monitor Hardware Overhead
Totally monitors for an -core system
By Cacti6.5 cache simulator
  16-core, 320KB cache
    4.10% to cache tag hardware area
    0.07% to whole cache hardware area
  64-core, 2.5MB
    12.00% to cache tag hardware area
    0.49% to whole cache hardware area
Thus, hardware area overhead is relatively small

## Slide 37: Experimental Parameters
Gem5 system simulator
  16-core
  2Ghz
  X86_64 ISA
Memory hierarchy parameters | 
Network | mesh topology
Coherence protocol | MOESI CMP directory
Link latency | 32 cycles
Private L1 cache | 4kB, 64B, 2-way, LRU, write-back, 3 cycles
Shared L2 cache | 320kB, 64B, 10-way, write-back, 25 cycles
DRAM | 350 cycles
Memory hierarchy parameters | 
Network | 
Coherence protocol | MOESI CMP directory
Link latency | 32 cycles
Private L1 cache | 4kB, 64B, 2-way, LRU, write-back, 3 cycles
Shared L2 cache | 320kB, 64B, 10-way, write-back, 25 cycles
DRAM | 350 cycles

## Slide 38: Controlled workload
Emulate a multi-application environment
  One core execute a benchmarking kernel
  Other cores execute streaming accessing patterns
a
a
Re-accessing
a
Re-accessing
a
Other applications
Long distance
Short distance